Exhibit A

1.	Amend Portland City Code 24.10.040 D, as follows:

24.10.040 D

D.	Residential code.  The provisions of the State of Oregon, Residential Specialty Code, 20052008 Edition, as published by the International Code Council, and known as the International Residential Code, 20032006 Edition, and amended by the Building Codes Division of the Oregon Department of Consumer and Business Services, including the appendices and standards adopted by the State of Oregon, is hereby adopted by reference.  Furthermore, in that Appendix AN is adopted by the State of Oregon as part of the 2005 Residential Specialty Code, Section AN109.4 is hereby specifically adopted and supercedes the provisions of Section AN103.2.3.  The Residential Specialty Code is on file in the Development Services Center of the City of Portland.

2.	Amend Section 24.50.020 General, Subsection D, as follows:

D.	The flood protection elevations and the floodway and floodway fringe areas specified by this Chapter, based on the 100-year flood elevations, are considered reasonable. Greater flood heights and more extensive floodway fringe areas associated with longer flood frequency occurrences may occur or the flood height and extent of flooding may be increased by human or natural causes, such as log jams, bridge openings restricted by debris, or changes in basin conditions. Areas within designated drainage districts and those areas not covered by adequate topographic maps may contain unmapped watercourses subject to flooding. The identification of designated flood hazard areas does not imply that lands outside of such areas will be free from flooding or flood damage. The City of Portland or any officer or employee thereof, or the Federal Insurance Administration shall not be liable for any flood damages that result from reliance on the provisions or designations of this Chapter or any administrative decision lawfully made thereunder.

3.	Amend Section 24.50.030 Flood Related Definitions, J through X as follows:

J.	"Flood Hazard Area" means any area which has been identified as subject to flooding.  Flood Insurance Study means the official report provided by the Federal Insurance Administration that contains information regarding flooding, discusses the engineering methods used to develop the Flood Insurance Rate Maps (FIRMs), includes flood profiles, and the water surface elevation of the base flood.

K.	“Flood Insurance Study” means the official report provided by the Federal Insurance Administration that contains information regarding flooding, discusses the engineering methods used to develop the Flood Insurance Rate Maps (FIRMs), includes flood profiles, and the water surface elevation of the base flood.

KL.	"Flood Insurance Rate Map (FIRM)" means the official map on which the Federal Insurance Administration has delineated the areas of special flood hazards.

LM.	"Flood or flooding" means a general and temporary condition of partial or complete inundation of normally dry land areas from the overflow of inland or tidal waters, and/or the unusual and rapid accumulation of runoff of surface waters from any source.

MN.	"Flood protection elevation" means the water surface elevation of the base flood plus a freeboard allowance.

NO.	"Floodplain" means the channel of watercourse and adjacent land areas which are subject to inundation by the base flood.

OP.	"Floodproofing" means any combination of structural and nonstructural additions, changes, or adjustments to structures which reduce or eliminate flood damage to real estate or improved real property, sanitary, and water facilities, structures, and their contents.

PQ.	"Floodway" means the channel of a river or other watercourse and the adjacent land areas that must be reserved in order to discharge the base flood without cumulatively increasing the water surface elevation more than one foot.  The actual floodway boundaries are computer activated and approximate.  These boundaries are depicted on the FIRM. Boundaries for other watercourses may be subject to identification by the Sewage System Administrator.  The width of the floodway for unidentified watercourses should not be less than 15 feet.

QR.	"Flood fringe area" means any area lying outside the floodway which is subject to flooding by a base flood and for which water surface elevations and floodway and flood fringe boundaries have been determined by a Flood Insurance Study and are shown on the FIRMs.  Boundaries for unidentified watercourses may be subject to identification by the Sewage System Administrator.

RS.	"Freeboard" means an additional height above the base flood level to account for factors that may contribute to flood heights greater than the height calculated for a selected size flood and floodway conditions, such as filling in the floodway fringe, wave action, effect of urbanization of the watershed, map inaccuracies, irregular stream cross sections, irregular constructions at bridges, and the uncertainties of flood discharge computations.

ST.	"Lowest Floor" means the lowest floor of the lowest enclosed area (including basement).  An unfinished or flood resistant enclosure, usable solely for parking of vehicles, building access or storage, in an area other than a basement area, is not considered a building’s lowest floor, provided that such enclosure is not built so as to render the structure in violation of the applicable non-elevation design requirements of this ordinance found at Section 24.50.060 F.2.

TU.	"Manufactured home" means a structure transportable in one or more sections, which is built on a permanent chassis and is designed for use with or without a permanent foundation when connected to the required utilities.  For flood plain management purposes, the term "manufactured home" also includes park trailers, travel trailers, and other similar vehicles placed on a site for greater than 180 consecutive days.  For insurance purposes, the term "manufactured home" does not include park trailers, travel trailers, and other similar vehicles.

UV.	"New construction" means structures for which the start of construction commenced on or after the effective date of this Chapter.

VW.	"New manufactured home park or manufactured home subdivision" means a parcel (or contiguous parcels) of land divided into two or more manufactured home lots for rent or sale for which the construction of facilities for servicing the lots on which the manufactured home is to be affixed (including as a minimum, the installation of utilities, either final site grading or the pouring of concrete pads and the construction of streets) is completed on or after the original date of this Chapter.  Start of construction includes substantial improvement, and means the date the building permit was issued, provided the actual start of construction, repair, reconstruction, placement or other improvement was within 180 days of the permit date.  The actual start means either the first placement of permanent construction of a structure on a site, such as the pouring of slab or footings, the installation of piles, the construction of columns, or any work beyond the stage of excavation; or the placement of a manufactured home on a foundation.  Permanent construction does not include land preparation, such as clearing, grading and filling; nor does it include the installation of streets, walkways, sanitary sewers, storm sewers, and/or drainage facilities; nor does it include excavation for a basement, footings, piers, or foundation or the erection of temporary forms; nor does it include the installation on the property of accessory buildings, such as garages or sheds not occupied as dwelling units or not part of the main structure.  Structure or accessory structure means, for the purposes of this Chapter, a walled and roofed building including a gas or liquid storage tank that is principally above ground.

WX.	"Substantial Improvement" means any repair, reconstruction, or improvement of a structure, the cost of which equals or exceeds 50 percent of the market value of the structure, either:

1.	Before the improvement or repair is started, or

2.	If the structure has been damaged, and is being restored, before the damage occurred. Substantial improvement is considered to occur when the first alteration of any wall, ceiling, floor, or other structural part of the building commences, whether or not that alteration affects the external dimensions of the structure.

The term does not, however, include either:

a.	Any project for improvement of a structure to comply with existing State or local health, sanitary, or safety code specifications which are solely necessary to assure safe living conditions, or

b.	Any alteration of a structure listed on the National Register of Historic Places or the State Inventory of Historic Places.  Variance means a grant of relief from the requirements of this ordinance which permits construction in a manner that would otherwise be prohibited by this ordinance.  Water surface elevation means the height of the water surface of the base flood for any point along the longitudinal course of a stream.  Watercourse means a channel in which a flow of water occurs, either continuously or intermittently, and if the latter, with some degree of regularity.  Watercourses may be either natural or artificial.

3.	Amend Section 24.50.050 Flood Hazard Areas and Flood Protection Elevations, Subsection G as follows:

G.	Johnson Creek FIRM FloorFlood Zone AO.  This flood zone represents areas of shallow flooding depth (1 to 3 feet) for which the depths of flooding are determined.  The flood protection elevation shall be the depth of flooding shown on the FIRM map plus two feet of freeboard above the highest adjacent grade.

4.	Amend Section 24.50.050 Flood Hazard Areas and Flood Protection Elevations, Subsection J as follows:

J.	Metro Flood Management Areas. Flood 1996 inundation areas shown on Metro Title 3 Water Quality and Flood Management Area Maps shall have a flood protection elevation which provides two feet of freeboard above the Flood 1996 level.  Flood 1996 inundation areas adjacent to Columbia River FIRM Flood Zone AE, Multnomah Drainage District No. 1, Peninsula Drainage District No. 2 Firm Zone AH and Columbia River FIRM Flood Zone A shall have freeboard of one foot.

5.	Amend Section 24.50.060 Provisions for Flood Hazard Reduction, Subsection F Special Flood Hazard Areas, Subsection 4 Nonresidential construction, as follows:

4.	Nonresidential construction. New construction and substantial improvement of any commercial, industrial, or other nonresidential structure shall either have the lowest floor, including basement, elevated to the level of the flood protection elevation, or, together with attendant utility and sanitary facilities, shall:

a.	Be floodproofed so that below the base flood protectionlevel elevation the structure is watertight with walls substantially impermeable to the passage of water;

(Subsections b through e unchanged)

6.	Amend Section 24.50.060 Provisions for Flood Hazard Reduction, Subsection F Special Flood Hazard Areas, Subsection 8 Balanced Cut and Fill Required, as follows:

8.	Balanced Cut and Fill Required. In all Flood Management Areas and Special Flood Hazard Areas of the City not addressed by Section 24.50.060 G, balanced cut and fill shall be required.  All fill placed at or below the flood protectionbase flood elevation shall be balanced with at least an equal amount of soil material removal.  Soil material removal shall be within the same flood hazard area identified in Section 24.50.050 A. through I.

a.	Excavation shall not be counted as compensating for fill if such areas will be filled with water in non-storm winter conditions.

b.	Temporary fills permitted during construction shall be removed.

7.	Amend City Code 25.01.020, as follows:

25.01.020	Scope - Oregon Plumbing Specialty Code.

This Title shall apply to all plumbing done within the City, except sewer facilities installed by the City Engineer through contract or by City work force in any public place or right-of-way for the disposal of sanitary or storm drainage; and water supply facilities installed by the Water Engineer through contract or City work force in any public place or right-of-way for supplying the water service.

The provisions of the Uniform Plumbing Code, 20032006 edition, including the appendix and installation standards, published by the International Association of Plumbing and Mechanical Officials, as amended by the Building Codes Division of the Oregon Department of Consumer and Business Services, and known as the 20052008 Edition of the Oregon Plumbing Specialty Code, are hereby adopted by reference.  The Plumbing Specialty Code is on file in the Development Services Center of the City of Portland.

8.	Repeal Portland City Code Section 25.01.030 in entirety.

9.	Amend Portland City Code 26.01.030, as follows:

26.01.030	Code Adoption.

The provisions of the State of Oregon Electrical Specialty Code, 20052008 Edition, as published by the National Fire Protection Association and known as the National Electrical Code (NEC) 20052008 Edition and amended by the Building Codes Division of the Oregon Department of Consumer and Business Services, including the appendices and Electrical Standards adopted by the State of Oregon, are hereby adopted by reference.

The provisions of the State of Oregon Residential Specialty Code, 2005 Edition, as published by the International Code Council as the International Residential Code, 2003 Edition and amended by the Building Codes Division of the Oregon Department of Consumer and Business Services including the appendices and standards adoped by the State of Oregon, is hereby adopted by reference. Furthermore, in that Appendix AN is adopted by the State of Oregon as a part of the 2005 Residential Specialty Code, Section AN109.4 is hereby specifically adopted and supercedes the provisions of Section AN103.2.3.

These codes and standards are on file in the Development Services Center of the City of Portland. This Title shall prevail except where specifically prohibited by the Oregon Revised Statutes and the Oregon Administrative Rules.

10.	Amend Portland City Code 26.02.050, as follows:

26.02.050	Electrical Code.

The Electrical Code shall mean the current State of Oregon Electrical Specialty Code, (including appendices and Electrical Standards) and the electrical provisions of the State of Oregon, Residential Specialty Code, 2005 Edition (including appendices and standards), as adopted by the State of Oregon.