## Slide 1: Residential Infill Project – Part 2
Bringing Portland Into Compliance with State Legislative Mandates for Middle Housing
Morgan Tracy
Project Manager
Sandra Wood
Principal Planner
Shannon Buono
Senior Planner
JP McNeil
City Planner

## Slide 2: What are the State mandates?
House Bill 2001 – requires cities to allow duplexes on all lots, and other middle housing (triplexes, fourplexes, cottage clusters, attached houses) on most lots.
Senate Bill 458 – requires cities to process land divisions for middle housing development, so that each dwelling unit can be sold on its own lot.

## Slide 3: RIP2 proposals
R10/R20 Zones (catching up with RIP1)
Floor area limits (smaller lots)
Duplexes (all lots)
Triplexes/Fourplexes (some lots)
More ADU options (some lots)
Visitable units
Affordable 4-6 plexes (some lots)
All single dwelling zones
Attached houses (most lots)
Cottage clusters (most lots)
Detached duplexes (most lots)
Modified ‘z’ overlay/update Landslide hazard map
Middle housing land divisions

## Slide 4: RIP2 scope
Area
RIP2 includes areas that were not part of RIP1 – i.e. R10 and R20 zones.
R2.5, R5 and R7 zones
(about 134,000 lots)
R10 and R20 zones
(about 16,000 lots)
RIP2
RIP1&2

## Slide 5: RIP2 scope
Housing types
RIP2 adds more housing types that were not included with RIP1 – i.e. cottage clusters and attached homes, in both RIP1 and RIP2 areas.
RIP1
RIP2

## Slide 6: RIP 2 – proposal #7 - Attached Houses
Attached units on separate lots
Higher density (to match triplex/fourplex density)
Look like plexes, but units always arranged side-by side
Regular land division
Credit: Brookfield Residential

## Slide 7: RIP 2 – proposal #8 -Cottage Clusters
3-16 detached units
900 sf footprint max
1,400 sf avg floor area
Common outdoor area
Credit: Propel Studio

## Slide 8: RIP 2 – Proposal #9 - Detached Duplex
Not required by HB2001
On sites with an existing house
25’ max height limit
Eligible for middle housing land division

## Slide 9: Recap of new housing types added with RIP1 and RIP2
House
House+ADU
Corner duplex
Prior to RIP: house, house w/ADU, corner lot duplex
All single dwelling zones

## Slide 10: Recap of new housing types added with RIP1 and RIP2
House
House+ADU
Corner duplex
Duplex
House+2 ADUs
Duplex+ADU
Triplex
Fourplex
Affordable 6plex
RIP1
R2.5, R5, R7 zones
RIP1 added: plexes, more ADU options and the deep affordability bonus sixplex

## Slide 11: Recap of new housing types added with RIP1 and RIP2
House
House+ADU
Corner duplex
Duplex
House+2 ADUs
Duplex+ADU
Triplex
Fourplex
Affordable 6plex
Attached Houses
Cottage Cluster
Detached Duplex
RIP2
All single dwelling zones

## Slide 12: Housing types required by HB2001
House
House+ADU
Corner duplex
Duplex
House+2 ADUs
Duplex+ADU
Triplex
Fourplex
Affordable 6plex
Attached Houses
Cottage Cluster
Detached Duplex
In areas of all single dwelling zones

## Slide 13
R10 and R20
Proposed ‘z’ Overlay
R2.5, R5, and R7
(~6,000 of 134,000 lots)
RIP2 Proposal #10 The ‘z’ overlay
(~18,500 of 150,000 lots)
(~12,500 of 16,000 lots)
Environmental
Landslide
Flood
Wildfire
Airport noise
Future industrial
Notes: Mention landslide hazard data update

## Slide 14: RIP2 Proposal #11 SB458 – Middle Housing Land Divisions
Zoning requirements apply to parent parcel as a whole
  coverage, setbacks, FAR, etc
Building code applies to all lots
Separate utilities to each unit
ADUs not permitted
No min lot size or street frontage requirements

## Slide 15: RIP2 Council Schedule
April 21 – Hearing
May 19 – Hearing and vote on amendments
June 1 – 1st Reading/vote
July 1 – Effective date

## Slide 16
Morgan Tracy
Project Manager

## Slide 17: A tale of two land divisions…
Attached houses (regular LD)
Review criteria apply (e.g. trees)
120 day max review
Lots function independently
Building permit after
Divided plexes (MHLD)
No discretionary criteria
119 day max review
Lots reliant on parent parcel
Concurrent building permit

## Slide 18: RIP1 - Deeper Affordability 4 to 6 plex
Not required by HB2001
Allow 4 to 6 units when:
  ½ of the units are at 60% MFI rental or 80% MFI ownership
  2 units are visitable
1.2 FAR allowed
35’ height allowed
Standard setbacks, building coverage, outdoor area requirements apply