## Slide 1
BLOCK A DESIGN ADVICE REVIEW SEPTEMBER 20, 2012 GBD ARCHITECTS Incorporated

## Slide 2
DESIGN ADVICE REQUEST SUMMARY
SITE OVERVIEW
DEFINITION & PURPOSE OF SUPERBLOCK REGULATIONS
MULTIPLE OWNERSHIP & BLOCK A REQUIREMENTS
AREA REQUIREMENS
AREA PROVIDED
PLAZA REQUIREMENTS
MODIFICATION
TIME ALLOWING
PROJECT REVIEW
MASSING AND MATERIALS
PRESENTATION OVERVIEW

## Slide 3
CONTEXT: LOCATED NORTH OF THE CONVENTION CENTER
SITE OVERVIEW
1

## Slide 4
BOUNDED BY MULTNOMAH AND MLK WITH HOLLDAY TO THE SOUTH & 2ND TO THE WEST
SITE OVERVIEW
1
NE MULTNOMAH
NE MLK BLVD
NE HOLLADAY
NE 2ND

## Slide 5
SITE OVERVIEW
1
Powells
Rembold Companies
PDC
Starterra
Byrnes
POWELLS
PDC
REMBOLD COMPANIES
STARTERRA
BYRNES
MULTIPLE OWNERSHIPS
POWELLS
REMBOLD
PROPERTIES
PDC
STARTERRA
BYRNES

## Slide 6
SUPERBLOCK CREATED WHEN THE CITY VACATED NE 3RD AND NE HASSALO
SUPERBLOCK DEFINITION
2
NE HASSALO
NE 3RD
Superblock regulations apply to all new development on sites that include 5,000 sf or more of vacated streets.
Area of vacated streets
36,739 SF
Area of Superblock
185,405 SF

## Slide 7
PURPOSE & 33.293.010 REQUIREMENTS
SUPERBLOCK PURPOSE
2
NE HASSALO
NE 3RD
The superblock chapter regulates the amount and location of open areas and walkways on large commercial sites where streets have been vacated.
The intent is to promote a pleasant and convenient walkway and open space system on the superblock that links to the adjacent buildings, to the public circulation system, and to any available public transit.
The requirement also promotes the maintenance of light, air and access that could be lost due to development on the vacated street.
Developments must provide walkways, landscaped areas and Public Plazas
(or Public Atriums)

## Slide 8
DEFINITION & REQUIREMENTS OF MULTIPLE OWNERSHIPS
MULTIPLE OWNERSHIPS
3
NE HASSALO
NE 3RD
In cases where a superblock contains multiple ownerships and only one ownership is being developed:
Each ownership will provide walkways, landscaped areas and plazas based on that ownership’s percentage of the total vacated street area
The required walkways, landscaped areas and plazas for each ownership must be integrated into the previously required walkways, landscape areas & plazas of the other ownerships in the superblock

## Slide 9
BLOCK A PERCENT CALCULATION
MULTIPLE OWNERSHIPS
3
NE HASSALO
NE 3RD
Each ownership will provide walkways, landscaped areas and plazas based on that ownership’s percentage of the total vacated street area
Area of Vacated Streets on Entire Superblock
36,739 SF
Area of Vacated Streets on Block A
12,901 SF
Calculation:
12,901 SF / 36,739 SF = 35%
Block A’s Percentage of Total Vacated Streets
35%
Block A % of Superblock
24%
35%

## Slide 10
BLOCK A – WALKWAYS, LANDSCAPE AREAS & PLAZA REQUIREMENTS
AREA REQUIREMENTS
4
6,430 SF
Walkway, Landscape Areas and Public Plazas must equal 50% of the total area of the vacated streets
Area of the Vacated Streets
36,739 SF
Walkway, Landscape and Public Plaza Area for the Entire Superblock
Calculation:
36,739 SF x 50% = 18,370 SF
Walkways, Landscape & Plaza Area Required for Block A
Calculation:
35% x 18,370 = 6,430 SF
6,430 SF

## Slide 11
AREA REQUIREMENTS
4
A public plaza must be provided with the superblock equal to 5% of the superblock land area
Plaza Area Required for the Entire Superblock
Calculation:
185,405 SF x 5% = 9,270 SF
9,270 SF
Plaza Area Required for
Block A
Calculation:
35% x 9,270 SF = 3,245 SF
3,245 SF
3,245 SF
BLOCK A – PLAZA REQUIREMENTS

## Slide 12
AREA PROVIDED
5
NE HASSALO
NE 3RD
Block A - Walkway Area Provided
2,384 SF
Block A – Landscape Area Provided
400 SF
Block A – Plaza Area Provided
4,643 SF (+1,398)
Block A – Total Area Provided
Calculation:
2,384 SF + 400 SF + 4,643 SF =
7,427 SF
7,427 SF (+ 997 SF)
Block A Plaza
3,245 SF
BLOCK A – WALKWAYS, LANDSCAPE & PLAZA PROVIDED

## Slide 13
PLAZA DEFINITION
PLAZA REQUIREMENTS
6
NE HASSALO
NE 3RD
PLAZA DEFINITION
An area generally open to the public on a controlled basis and used for passive recreational activities and relaxation. Plazas are paved areas typically provided with amenities, such as seating, drinking and ornamental fountains, art, trees, and landscaping, for use by pedestrians.
RATIO REQUIREMENT
The ratio of the length to the width of a plaza in a superblock may not exceed
3 to 1

## Slide 14
PLAZA REQUIREMENTS
6
NE HASSALO
NE 3RD
Due to the odd shape, we looked at the plaza as a series of spaces
A: 1,988 SF
71’x28’
1:2.5
B: 1,000 SF
40’x25’
1:1.6
C: 900 SF
45’x20’
1:2.5
Note: The entire plaza area is not accounted for in these areas. An additional 755 SF is located in the triangle between A and B, and the triangle between B and C.
Block A Plaza
3,245 SF
PLAZA - RATIO REQUIREMENTS
A
B
C
A
B
C

## Slide 15
MODIFICATION
7
NE HASSALO
NE 3RD
Block A Plaza
3,245 SF
MODIFICATION OF PLAZA RATIO
DOES THE COMMISSION FEEL THAT A MODIFICATION ON THE PROPOSED MEASUREMENT METHODOLOGY FOR THE PLAZA RATIO IS APPROVABLE ?
Criteria for Modification Approval:
  The resulting development will better meet the applicable design guidelines; and on balance, the proposal will be consistent with the purpose of the standards for which a modification is requested
Purpose of Superblock
  The intent is to promote a pleasant and convenient walkway and open space system on the superblock that links to the adjacent buildings, to the public circulation system, and to any available public transit.
  The requirement also promotes the maintenance of light, air and access that could be lost due to development on the vacated street.
Justification:
  Providing private drives which will be built to meet Lloyd District Standards and for all intents an purposes will act and feel like a standard street in addition to meeting all of the walkway, landscape and plaza area requirements will not only meet the intent, but will provide better connections and more access to light and air than would otherwise be met meeting the standards alone.

## Slide 16
PROJECT REVIEW
8
NE HASSALO
NE 3RD
Block A Plaza
3,245 SF
CONTEXT

## Slide 17
PROJECT REVIEW
8
NE HASSALO
NE 3RD
Block A Plaza
3,245 SF
CONTEXT

## Slide 18
PROJECT REVIEW
8
NE HASSALO
NE 3RD
Block A Plaza
3,245 SF
BELOW GRADE PARKING PLAN

## Slide 19
PROJECT REVIEW
8
NE HASSALO
NE 3RD
Block A Plaza
3,245 SF
GROUND FLOOR PLAN

## Slide 20
PROJECT REVIEW
8
NE HASSALO
NE 3RD
Block A Plaza
3,245 SF
TYPICAL FLOOR PLAN

## Slide 21
MATERIALS & MASSING
8
NE HASSALO
NE 3RD
Block A Plaza
3,245 SF
INTERSETION OF MULTNOMAH AND 3RD

## Slide 22
MATERIALS & MASSING
8
NE HASSALO
NE 3RD
Block A Plaza
3,245 SF
INTERSETION OF 3RD AND HASSALO

## Slide 23
MATERIALS & MASSING
8
NE HASSALO
NE 3RD
Block A Plaza
3,245 SF
INTERSECTION HASSALO & MLK

## Slide 24
SITE OVERVIEW
SEPTEMBER 20, 2012
BLOCK A – CONVENTION CENTER
DESIGN ADVICE REQUEST
300 NE MULTNOMAH