## Slide 1: HAZELWOOD PLAZA 222 NE 102nd Ave. Portland, OR 61 RESIDENTIAL UNITS
ALBERTO RINKEVICH RICARDO BERDICHEVSKY
ARCHITECS QUAIL COURT MANAGEMENT
4810 SW LOWELL CT. PORTLAND, OR 97221 3570 RIVER PARKWAY PORTLAND, OR 9729
503-927-1758 FAX 503-922-2613 503-477-4587 FAX 503-954-2612

## Slide 2: Project location: 222 NE 102nd. Ave. Portland, OR Neighborhood: Hazelwood Plan District: Gateway Plan district Design Guidelines: Gateway regional district Zoning: CMd, Mixed Residential/Commercial with design Overlay Maximum building height : 75 feet Floor area ratio (FAR): Max. 4:1 Min. 1:1 Parking: Not required, 52 provided Bicycle parking: Long term : 8 provided, 6 required Short term: 110 provided, 61 required

## Slide 3: Site Analysis

## Slide 4: Site Analysis

## Slide 5
Design Strategy
Answer to the government's social housing demands
Rigorous formal and constructive order
To articulate and break the longitudinal dimension of the building defined by the urban parameters
Emphasize the facades composition utilizing materials colors and textures
To achieve budget objectives
Building to be easily identifiable by the end user

## Slide 6: Project Description
Property Address
No. Residential Units
Net Rentable Area (NRSF)
Common Area
Gross Building Area
No. Buildings
No. of Floors
Site Area
Building Construction
Roof Type
Building Exterior
HVAC System
Electrical Metering
Water Metering
222 NE 102nd Avenue
61
46,696 sq. ft.
12,322 sq. ft.
59,018 sq. ft.
1
5 residential floors with tuck under parking
24,338 sq. ft.
Wood frame
Green composite / seamed metal
Corrugated metal panel and prefinished
cement board siding, metal balcony
Split air conditioners
Individual
Individual

## Slide 7
Vicinity
GATEWAY
TRANSIT CENTER
i-205 SHOPPING MALL
SE 102 ND / SE WASHINGTON ST.

## Slide 8
Vicinity photos

## Slide 9: Site – current photos
the site is tapered, with one long side facing the street and one long side bounded by four small properties
the site was rezoned (consolidate 4 in 1 big lot) to replace four dilapidated townhouses with a 61-unit apartment building.

## Slide 10
Site Plan
Site + Roof Plan
Site Section
Site plans & section
The building gently steps up in scale from the lower two story residences to the taller, denser 102nd. Avenue

## Slide 11: First Floor Plan

## Slide 12: Type Floor Plan

## Slide 13: Fifth Floor Plan

## Slide 14: Roof Plan

## Slide 15: Apartment Types
Unit Type Quantity Sq. Ft.
1 BR/1 BA 28 652
1 BR/1 BA 04 670
2 BR/1BA 12 985
2 BR/2 BA 16 985
1 BR/1BA 1 540

## Slide 16
Apartment Types - Plans

## Slide 17: Special Units and Core

## Slide 18
Elevations
PREFINISHED
CEMENT BOARD
PREFINISHED
CEMENT BOARD
PREFINISHED
CEMENT BOARD
CORRUGATED METAL PANEL
PREFINISHED
CEMENT BOARD
CURTAIN WALL
COMPOSITE ROOF
METAL RAILING

## Slide 19
Elevations
The bold exterior colors reflect the design strategy of identification and composition, the long west façade engages in a fluent dialog with the surrounding and make a friendly pedestrian environment

## Slide 20
Wall section & plan details

## Slide 21
Wall section & plan details
METAL SILL
METAL TRIM
HEADER

## Slide 22
Axonometric view & wall section

## Slide 23
Wall section details + finishes

## Slide 24
Axonometric view + finishes
Corrugated metal panel
Prefinished cement board

## Slide 25
Modifications Request
Ground Floor Active Use Requirement (33.526.280 D.2)
The Ground Floor Active Use areas requires 25'-0" deep in interior spaces that front onto a sidewalk.
Request: in order to allow a better screening of the parking garage from the 102nd. street and a more efficient design and operation of the parking garage we request to reduce to 13'-2" deep of the apartments located at the front of the building.
Short-Term Bicycle Parking (33.266.220 A.2b(3))
Building with one main entrance. For a building with one main entrance, the bicycle parking must be within 50 feet of the main entrance to the building as measured along the most direct pedestrian access route .
Request: The short-term bicycle parking is located between two apartments in a public landscaped sitting area. This is one of the recessed areas along the 102nd. Ave. resulting from the intension to break the long front elevation to avoid an extended massive building. The distance between the main access to the bicycle parking is 58 feet instead of the 50 required.

## Slide 26
Parking area setbacks and landscaping (33.266.130 G.3a)
Amount of interior landscaping required. In all zones, interior landscaping must be provided for sites where there are more than 10 parking spaces on the entire site. At least 45 square feet of interior
landscaped area must be provided for each parking space.
Request: 26 of the parking spots located in the back side of the parking lot are partially exposed. As a result of this situation the code demand 1,170 sq.ft. of interior landscape. Our request is to be exempted from this item.
.

## Slide 27
Sormwater Management
The proposed stormwater management at this stage of the building design is based on the SWMM requirements. Is a mixed solution composed by the use of 6 drywells (4 feet diameter X 5 feet H as per Chapter 2 Exhibits 2.30 and 2.31) serving an impervious area of 3,000 sq,ft each one, combined with a 1,600 sqf. concrete planter (detail as per Appendix G, detail SW-130) located along the east property line, see first fl. plan. All the drywells are located five feet from the property line and at list 10 feet distance from any structural component.

## Slide 28: General Images

## Slide 29: Pedestrian Images

## Slide 30: Same materials used in other buildings in Portland

## Slide 33: Detailed examples

## Slide 37: Composite Roof examples