## Slide 1: Mixed Use Zones Project PSC Work Session – June 28, 2016

## Slide 2: Inclusionary Housing Program Concept

## Slide 3
June 2016
July 2016
August 2016
September 2016
October 2016
December 2016
City Council Hearing on IH Program and Zoning Code
PSC Hearing and Recommendation
IH Code Concept Development and Staff Coordination
Draft Code Concept Proposal
Panel of Experts Review
Community Forums
Discussion Draft
Outreach to Stakeholder Groups
Draft Proposed Zoning Code
Commissioner Saltzman Program Recommendations
Process/Timeline

## Slide 4
Staff Recommendation:
Retain proposed structure of base and bonus FAR allowances, subject to future changes resulting from Inclusionary Zoning/Housing work.
Topic 3: Base and Bonus FAR allowances
Notes: 4

## Slide 5
Topic 3: Zoning Concept: Bonus for Community Benefits
Setting “base” and “bonus” levels will be a key part of concept modeling, testing and refinement.
Current allowances
Base allowance
Bonus allowance

## Slide 6
Topic 3: FAR Recommendations
 | Commercial Mixed Use 1 (CM1) | Commercial Mixed Use 2 (CM2) | Commercial Mixed Use 3 (CM3) | Commercial Employment (CE)
Preliminary Form |  |  |  | 
Examples |  |  |  | 
Height Limit FAR | 1.5:1 | 2.5:1 | 3:1 | 2.5:1
Bonus Ht Limit Bonus FAR | 2.5:1 | 4:1 | 5:1 | 3:1

## Slide 7
CM1 Zone
 | Small Scale Zones |  |  | 
 | CM1 | CN1 | CN2 | CO1
Height – Maximum Base (feet) | 35’ | 30’ | 30’ | 30’
Height – Maximum with Bonus | 35’ | 30’ | 30’ | 30’
FAR – Maximum Base | 1.5:1 | .75:1 | .75:1 | .75:1
FAR – Maximum* w/ Bonus | 2.5:1 | 2.5:1 | 2:1 | 1.5:1
* existing = estimated max for housing |  |  |  | 
Commercial |  |  |  | 
Retail Sales And Service | L | L | Y | N
Office | L | L | Y | Y
Quick Vehicle Servicing | N | N | L | N
Vehicle Repair | N | N | N | N
Commercial Parking | N | N | N | N
Self-Service Storage | N | N | N | N
Residential |  |  |  | 
Household Living | Y | Y | Y | Y
Group Living | L/CU | L/CU | L/CU | L/CU
Industrial |  |  |  | 
Manufacturing and Production | L | L/CU | L/CU | N
Warehouse and Freight Movement | N | N | N | N
Wholesale Sales | N | N | N | N
Industrial Service | N | N | N | N
Institutional |  |  |  | 
Basic Utilities | Y/CU | Y/CU | Y/CU | Y/CU
Community Service | L/CU | L/CU | L/CU | L/CU
Parks and Open Areas | Y | Y | Y | Y
Schools, Religious Institutions, etc. | Y | Y | Y | Y

## Slide 8
CM2 Zone
 | Medium Scale Zones |  |  | 
 | CM2 | CO2 | CM | CS
Height – Maximum Base (feet) | 45’ | 45’ | 45’ | 45’
Height – Maximum with Bonus | 55’* | 45’ | 45’ | 45’
FAR – Maximum Base | 2.5:1 | 2:1 | 1:1 | 3:1
FAR – Maximum* w/ Bonus | 4:1 | 2.6:1 | 4:1 | 4:1
* existing = estimated max for housing |  |  |  | 
Commercial |  |  |  | 
Retail Sales And Service | Y | L | L | Y
Office | Y | Y | L | Y
Quick Vehicle Servicing | N | N | N | N
Vehicle Repair | Y | N | N | Y
Commercial Parking | L | N | N | Y
Self-Service Storage | N | N | N | N
Residential |  |  |  | 
Household Living | Y | Y | Y | Y
Group Living | L/CU | L/CU | L/CU | L/CU
Industrial |  |  |  | 
Manufacturing and Production | L | N | L/CU | L/CU
Warehouse and Freight Movement | N | N | N | N
Wholesale Sales | L | N | L | L
Industrial Service | CU | N | N | CU
Institutional |  |  |  | 
Basic Utilities | Y/CU | Y/CU | Y/CU | Y/CU
Community Service | L/CU | L/CU | L/CU | L/CU
Parks and Open Areas | Y | Y | Y | Y
Schools, Religious Institutions, etc. | Y | Y | Y | Y

## Slide 9
CE Zone
 | Medium Scale Zones | 
 | CE | CG
Height – Maximum Base (feet) | 45’ | 45’
Height – Maximum with Bonus | 45’ | 45’
FAR – Maximum Base | 2.5:1 | 3:1
FAR – Maximum* w/ Bonus | 3:1 | 3.4:1
* existing = estimated max for housing |  | 
Commercial |  | 
Retail Sales And Service | Y | Y
Office | Y | Y
Quick Vehicle Servicing | Y | Y
Vehicle Repair | Y | Y
Commercial Parking | Y | CU
Self-Service Storage | Y | L
Residential |  | 
Household Living | Y | Y
Group Living | L/CU | L/CU
Industrial |  | 
Manufacturing and Production | L | L/CU
Warehouse and Freight Movement | L | CU
Wholesale Sales | L | L
Industrial Service | CU | CU
Institutional |  | 
Basic Utilities | Y/CU | Y/CU
Community Service | L/CU | L/CU
Parks and Open Areas | Y | Y
Schools, Religious Institutions, etc. | Y | Y

## Slide 10
CM3 Zone
 | Large Scale Zones |  | 
 | CM3 | EX | CX
Height – Maximum Base (feet) | 65’ | 65’ | 75’
Height – Maximum with Bonus | 75’ | 65’ | 75’
FAR – Maximum Base | 3:1 | 3:1 | 4:1
FAR – Maximum* w/ Bonus | 5:1 | 3:1 | 7:1
* existing = estimated max for housing |  |  | 
Commercial |  |  | 
Retail Sales And Service | Y | Y | Y
Office | Y | Y | Y
Quick Vehicle Servicing | N | N | L
Vehicle Repair | Y | Y | L
Commercial Parking | L | CU | CU
Self-Service Storage | L | L | L
Residential |  |  | 
Household Living | Y | Y | Y
Group Living | L/CU | L/CU | L/CU
Industrial |  |  | 
Manufacturing and Production | L | Y | L/CU
Warehouse and Freight Movement | L | Y | N
Wholesale Sales | L | Y | L
Industrial Service | CU | Y | CU
Institutional |  |  | 
Basic Utilities | Y/CU | Y/CU | Y/CU
Community Service | L/CU | L | L/CU
Parks and Open Areas | Y | Y | Y
Schools, Religious Institutions, etc. | Y | Y | Y

## Slide 11
Topic 3: FAR Base and Bonus Analysis
CM1
CM2
CM3

## Slide 12
Staff Recommendation:
Retain proposed height limits.
Allow 3-foot additional height for high ground floor citywide.
Retain step-downs to adjacent Residential zones.
Retain bonus step-backs in CM2, CM3 zones.
Remove step-back over 55’ in CM3 zone on narrow streets.
Retain building articulation and length standards.
Topic 4: Development and Design standards
Notes: 12

## Slide 13
Topic 3: FAR Recommendations
 | Commercial Mixed Use 1 (CM1) | Commercial Mixed Use 2 (CM2) | Commercial Mixed Use 3 (CM3) | Commercial Employment (CE)
Preliminary Form |  |  |  | 
Examples |  |  |  | 
Height Limit FAR | 35’ (3) | 45’ (4) | 65’ (6) | 45’ (4)
Bonus Ht Limit Bonus FAR | 35’ (3) | 55’ (5)* * In key locations | 75’ (7) | 45’ (4)

## Slide 14
Topic 4: Height Alternative – CM1

## Slide 15
Height Alternative - CE

## Slide 16
Height Alternative – CM2

## Slide 17
Height Alternative – CM2 Bonus

## Slide 18
Height Alternative – CM3

## Slide 19
Height Alternative – CM3 Bonus

## Slide 20
Building Form Standards
Step Down Height and Building Articulation
“Step down”
Adjacent to lower-density residential zones
“Step back”
For bonus height
CM3 on narrow streets

## Slide 21
 | CM1 | CM2 and CE | CM3
Step Downs to Residential Zones | Never required | Adjacent to SFR zones | Adjacent to SFR zones and R3 – R1 MFR zones
Front Step Backs | Never required | Only required for bonus height above 4 stories (45’) | Required for bonus height above 6 stories (65’) and on narrow streets above 5 stories (55’)
When Step Downs or Step Backs Are Required

## Slide 22: Addresses community concerns about need for scale transitions adjacent to single-dwelling zoning
Height Step Downs to Residential Zoning

## Slide 23: Within 25’ of abutting residential zones: - Height limited to 35’ adjacent to SFR zones - Height limited to 45’ adjacent to R3 – R1 MFR zones
Height Step Downs to Residential Zones
MUZ Proposal

## Slide 24: Map of where height transitions will apply
Height Step Downs to Residential Zoning

## Slide 25
Bonus height step backs Solar access modeling for CM2 zone: both 4-stories and 5th story bonus preserve solar access across the street (Spring and Fall equinox)
Front Step Backs

## Slide 26
Front Step Backs - Examples
Step backs not required on secondary streets
Mixed use zoning typically less continuous on side streets
Avoids costs and design issues of step backs on all frontages

## Slide 27
Bonus height step backs
Responds to community concerns about building scale
Retains base zone street wall height, stepping back additional bonus height to minimize appearance of greater scale
Front Step Backs

## Slide 28
Bonus height step backs
Responds to community concerns about building scale
Retains base zone street wall height, stepping back additional bonus height to minimize appearance of greater scale
Front Step Backs

## Slide 29
CM3 zone along narrow streets:
Limit street wall height to 55’ along streets with less than 70 feet of ROW
Responds to solar access and street space enclosure considerations
CM3 - Front Step Backs (drop from proposal)
Height-to-street-width analysis

## Slide 30
CM3 zone along narrow streets
CM3 Front Step Backs (drop from proposal)
Some areas where CM3 step downs (above 5th story) would apply

## Slide 31
Façade Articulation
  Façade Articulation:
  CM2: required when over 35’ and over 3500 SF area
  CM3: required when over 45’ and over 4500 SF area
  Only counts façade planes within 20 feet of lot line

## Slide 32
  Examples providing 25% (or more) façade articulation
  - can be met through a variety of design approaches
Façade Articulation

## Slide 33
  Examples that would not require façade articulation
  ( façades smaller than triggering threshold )
CM2
(two separate façade areas)
CM3
Façade Articulation

## Slide 34: Responds to community interest in continuing the fine grain development patterns of neighborhood mixed use areas, avoiding “monolithic” buildings.
Building Length Limits
Divided building volumes
Building with façade length exceeding the common 200’ pattern

## Slide 35: Building Length - Limits building length to 200’ close to street frontages
Building Length Limits

## Slide 36
Staff Recommendation:
CE zone: allow drive throughs and Quick Vehicle Servicing uses.
CM1, CM2, CM3: allow existing drive throughs and Quick Vehicle Servicing uses; prohibit new facilities.
Revise code to allow “Click and Collect” type facilities.
Retain DT + QVS prohibition in Centers Main Street overlay.
Revise buffering standards adjacent to Residential zones.
Topic 5: Drive Thrus; QVS; development standards
Notes: 36

## Slide 37
Insert Maps
Topic 5: Drive Thrus; QVS; development standards
Notes: 37

## Slide 38
Insert Maps
Topic 5: Drive Thrus; QVS; development standards
Notes: 38

## Slide 39
Staff Recommendation:
Limited CE zone changes in response to requests.
Consider limited RTF recommendations for CE zoning.
Consider limited expansion of CE zoning based on Policy 4.24:
“Prohibit drive-through facilities in the Central City and limit development of new ones in the Inner Ring Districts and centers in order to support a pedestrian-oriented environment.”
Retain proposed development standards.
Topic 6: CE Zoning - grocery, etc.; Development standards
Notes: 39

## Slide 40
Centers Map
Proposed Zoning Map
Notes: 40

## Slide 41
Centers Map
CE Requests + RTF Recommendations
Notes: 41

## Slide 42
Centers Map
CE Requests
Notes: 42

## Slide 43
Centers Map
CE Requests + RTF Recommendations
Notes: 43

## Slide 44
Centers Map
CE Requests + RTF Recommendations
Notes: 44

## Slide 45
Map Broad CE Allowances in CM1
CE/Drive Thru Policy Expansion Areas – CM1
Notes: 45

## Slide 46
Map Broad CE Allowances in CM1
CE/Drive Thru Policy Expansion Areas – CM2
Notes: 46

## Slide 47
Insert Maps
Development Standards
Notes: 47

## Slide 48
Insert Maps
Development Standards
Notes: 48

## Slide 49
Insert Maps
Development Standards
Notes: 49

## Slide 50
Insert Maps
Development Standards
Notes: 50

## Slide 51
Insert Maps
Auto-Accommodating Development
Notes: 51

## Slide 52
Alternative maximum building setback
for large retailers
Provides flexibility for shopping centers.
Allows large retail buildings to be set behind parking, when smaller secondary buildings are built close to public streets.
Proposed Draft reduces qualifying threshold from a 100,000 SF to 60,000 SF retail building.
Development Standards
Notes: 52

## Slide 53
Staff Recommendation:
Tentatively approve staff recommendations shown in items 7.1 to 7.5.
Provide direction on 7.1.F and 7.5.A.
Review final code prior to August 9, 2016 work session.
Topic 7: Code Issues raised in testimony and identified by: PSC; Design, Historic Landmarks and Urban Forestry Commissions; BDS; BPS
Notes: 53

## Slide 54
Ground Floor Options for Residential Uses
- Design to accommodate future commercial uses, or
- Setback or elevate units for privacy
Topic 7: Street Frontage Design

## Slide 55
Require all ground level units to have separate entrances?
Allow as an option.
Continue to allow other configurations that use shared entrances.
Street Frontage Design
Historic examples with shared entrances

## Slide 56: Side Setback Requirements Require a minimum of five feet between residential windows and property lines
Topic 7: Residential Livability Standards

## Slide 57
Topic 7: Ground Floor Windows
  Ground Floor Windows
  40% window standards is increase over current 25%
  Accommodates a range of uses – office, car repair, medical, etc.
  60% standard is geared to retail – strategically applied

## Slide 58
Topic 7: CM1 Expand Hours Limitations to 15K SF lots

## Slide 59: Resource Slides